## Slide 1
CONTROLLED ACCESS
In controlled access, the stations consult one another to find which station has the right to send. A station cannot send unless it has been authorized by other stations.

## Slide 2
Reservation access method

## Slide 3
Select and poll functions in polling access method

## Slide 4
Logical ring and physical topology in token-passing access method

## Slide 5
Wired LANs: Ethernet

## Slide 6
IEEE STANDARDS
In 1985, the Computer Society of the IEEE started a project, called Project 802, to set standards to enable intercommunication among equipment from a variety of manufacturers. Project 802 is a way of specifying functions of the physical layer and the data link layer of major LAN protocols.

## Slide 7
IEEE standard for LANs

## Slide 8
Ethernet evolution through four generations

## Slide 9
802.3 MAC frame

## Slide 10
Minimum and maximum lengths

## Slide 11
Frame length:
Minimum: 64 bytes (512 bits) Maximum: 1518 bytes (12,144 bits)

## Slide 12
Example of an Ethernet address in hexadecimal notation

## Slide 13
Unicast and multicast addresses

## Slide 14
The least significant bit of the first byte defines the type of address. If the bit is 0, the address is unicast; otherwise, it is multicast.

## Slide 15
The broadcast destination address is a special case of the multicast address in which all bits are 1s.

## Slide 16
Define the type of the following destination addresses:
a. 4A:30:10:21:10:1A b. 47:20:1B:2E:08:EE
c. FF:FF:FF:FF:FF:FF
Solution
To find the type of the address, we need to look at the second hexadecimal digit from the left. If it is even, the address is unicast. If it is odd, the address is multicast. If all digits are F’s, the address is broadcast. Therefore, we have the following:
a. This is a unicast address because A in binary is 1010.
b. This is a multicast address because 7 in binary is 0111.
c. This is a broadcast address because all digits are F’s.
Example

## Slide 17
Show how the address 47:20:1B:2E:08:EE is sent out on line.
Solution
The address is sent left-to-right, byte by byte; for each byte, it is sent right-to-left, bit by bit, as shown below:
Example

## Slide 19
Categories of Standard Ethernet

## Slide 20
Encoding in a Standard Ethernet implementation

## Slide 21
10Base5 implementation

## Slide 22
10Base2 implementation

## Slide 23
10Base-T implementation

## Slide 24
10Base-F implementation

## Slide 25
Table Summary of Standard Ethernet implementations