## Slide 1: Flow Control chap-7

## Slide 2: Data Link Control Protocols
Physical layer concentrates on sending signals over transmission link
More control and management is needed to send data over data communications link
  Frame synchronization: start and end of each frame
  Flow control: ensure sender does not send too fast for receiver
  Error control: correct bit errors introduced by transmission system
  Addressing: must specify identity of two stations communicating
  Control and data: receiver must distinguish between control and data information
  Link management: setup and maintain the link
We will focus on Flow Control and Error Control

## Slide 3: Flow Control
Flow control aims to ensure sending entity does not overwhelm receiving entity.
  If sender sends too fast for receiver, then buffer may overflow
  Result of buffer overflow: data is lost, possibly need to retransmit, which reduces performance
  Flow control tries to prevent buffer overflow
  Assume no errors but varying delays

## Slide 5: Model of Frame Transmission

## Slide 8: Stop-and-Wait Flow Control
Frame Types
  DATA: contains information to be sent
  ACKnowledgement: acknowledges receipt of data
Rules
  Source transmits a DATA frame
  Source waits for ACK frame before sending next DATA frame
  Destination receives DATA frame and replies with an ACK if ready for more data
  Destination can stop flow of data by not sending ACK

## Slide 9: Stop-and-Wait Flow Control

## Slide 10: Stop and Wait Link Utilization
Propagation delay is the time it takes for a bit to travel from sender to receiver, depends on
transmission media and
the distance between sender and receiver
B = R x (d/V)
B: length of the link in bits
R: data rate of the link, in bps
d: length or distance of the link in meters
V: velocity of propagation, in m/s
a = B/L
a: the propagation delay (with frame tx time = 1)
L: the number of bits in the frame
Propagation delay=d/V
Round-Trip Time = 2 × propagation delay

## Slide 11: Stop and Wait Link Utilization

## Slide 15: What Size Frames To Use?
Protocols often limit size of packets (frames), i.e. maximum number of bytes of data or payload
Large frames minimize header overheads
Small frames:
Allow more data to be sent when receive buffers are limited
Introduce small overhead if a retransmission is required
Allow fair sharing amongst multiple users
Optimal packet size depends on overheads, and desired throughput and delay performance

## Slide 16: Efficiency of Stop-and-Wait Flow Control
Efficiency n, for stop-and-wait flow control:
where: Data, Hdr, Ack are transmission times of original data in DATA frame, header in DATA frame and ACK frame respectively; Prop is link propagation time

## Slide 17: Sliding-Window Flow Control
Stop-and-wait allows only 1 frame to be in transit at a time
Sliding-window flow control allows multiple frames to be in transit at a time
Sequence Numbers
Each frame header contains k-bit sequence number (wraps back to 0 after 2k -1)
Keep track of frames sent and acknowledged

## Slide 18: Sliding-Window Flow Control
The Sender
Sender is allowed to send up to W frames without receiving ACK
Sender records:
  Last frame acknowledged
  Last frame transmitted
  Current window size

## Slide 19: Sliding-Window Flow Control
The Receiver
Receiver has buffer space for W frames
Receiver records:
  Last frame acknowledged
  Last frame received
  Current window size
Receiver sends an ACK (or Receiver Ready, RR) frame
ACK contains sequence number of next expected DATAframe

## Slide 20: Example

## Slide 23: Additional Features of Sliding Window
Receive Not Ready frame: acknowledges received frames but does not allow any more data
Piggybacking: DATA frame header contains sequence number of DATA and sequence number of ACK (acknowledgement number)
If no DATA to send, normal ACK is transmitted
If no new ACK, previous ACK number is repeated in DATA frame

## Slide 24: Example
A channel has a data rate of 4 kbps and a propagation delay of 20 ms. For what range of frame sizes does stop-and-wait give an efficiency of at least 50%?

## Slide 25: Stop-and-Wait Flow Control
Station sends F1
1
Station sends an acknowledgment.
2
Station sends F2
3
Station sends an acknowledgment.
4
Station sends Fn
5
Station sends an acknowledgment.
6

## Slide 29
bgb[AT]tezu.ernet.in

## Slide 30: Example
A sender sends a series of frame to the same destination using 5-bit sequence numbers. If the sequence number starts with 0, what is the sequence number of 101th frame?

## Slide 31
A five-bit sequence number can create sequence numbers from 0 to 31
The sequence number in the Nth frame is (N mod 32)
101th frame has the sequence number (101 mod 32) or 5.

## Slide 32: Calculate efficiency

## Slide 39: Utilization
U=1 when W≥2a+1
U=W/2a+1 when W<2a+1

## Slide 40: Example
Consider the use of 1000-bit frames on a 1-Mbps satellite channel with a 270-ms delay. What is the maximum link utilization for
  Stop-and-wait flow control?
  Continuous flow control with a window size of 7?
  Continuous flow control with a window size of 127?
  Continuous flow control with a window size of 255?

## Slide 41: L=103, R=106
a= propagation Time/(L/R)
a=270 ×10−3/(103/ 106) = 270
U = 1/(1 + 2a) = 1/541 = 0.002
U = W/(1 + 2a) = 7/541 = 0.013
U = 127/541 = 0.23
U = 255/541 = 0.47

## Slide 42: Error Control
Need to detect and correct errors such as:
Lost frames: frame not received
Damaged frames: frame received with errors
Common techniques used:
Error detection and FEC
Positive acknowledgment: destination returns a positive ACK after successfully receiving error-free frames
Retransmission after timeout: source retransmits a frame that has not been ACKed after predetermined time
Negative acknowledgement and retransmission: destination returns negative ACK for frames in which an error is detected

## Slide 43
Last 3 techniques are called automatic repeat request (ARQ). Three versions:
  Stop-and-wait ARQ
  Go-back-N ARQ
  Selective-reject ARQ

## Slide 44: Stop-and-Wait ARQ
Based on Stop-and-Wait flow control
Source transmits single frame, starts timer and maintains copy
If ACK received, stop timer and transmit next frame
If no ACK received before timer expires, retransmit copy of frame
Destination sends ACK if frame received (with no errors); if damaged frame, then discard frame
Frames have 1-bit sequence number (alternate between 0 and 1)
Used for destination to distinguish between duplicate DATA frames in case of damaged ACK
Stop-and-Wait ARQ is simple, but inefficient

## Slide 46: Example
A system uses the Stop-and-Wait ARQ Protocol. If each frame carries 1000 bits of data, how long does it take to send 1 million bits of data if the distance between the sender and receiver is 5000 Km and the propagation speed is 2 x 108 m? Ignore transmission, waiting, and processing delays. We assume no data or control frame is lost or damaged.

## Slide 47
  Propagation delay=d/V
d=5000km=5 x 106 m, V= 2 x 108 m
Propagation delay=5 x 106 / 2 x 108 =25ms
Nr of frame=1000000/1000=1000
Time delay for one successful frame delivery is 50ms(Ignore transmission, waiting, and processing delays. We assume no data or control frame is lost or damaged)
For 1000 frame, time delay=1000x50ms=50s